## Slide 1: IO MOLP models for Energy-Environment-Economy (E3) Planning
Carla Oliveira Henriques
coliv@inescc.pt; chenriques@iscac.pt
INESC Coimbra, Portugal
ISCAC Business School, Polytechnic Institute of Coimbra, Portugal
Energy for Sustainability Initiative (EFS-MIT Portugal), University of Coimbra
Mathematical Models and Methods for Energy Optimization, Budapest

## Slide 2: Outline
The Energy Sector and OR
  Energy-Environment-Economy models
    IO MOLP models (why?)
      Some basic features on IO
      Theoretical underpinning of IO MOLP models
      IO hybrid approaches
      Uncertainty handling of IO MOLP models
      A review on IO MOLP models
        IO LP models
        IO MOLP models
        IO LP and IO MOLP with uncertainty handling techniques
        LP dynamic IO models and MOLP dynamic IO models
        IO LP and IO MOLP with Data Envelopment Analysis (DEA)
        MOLP techniques for updating the IO matrix
    Conclusions

## Slide 3: The Energy sector and OR
The energy sector has been a fertile ground for the application of operational research (OR) models and methods
The first historical applications of multi-objective optimization (MOO) / multi-criteria analysis (MCA) in energy planning date back to the late 1970s, namely concerning power generation expansion planning or the choice of sites for nuclear and fossil-fired generation plants.
The need to consider explicitly multiple uses of water resource systems or environmental aspects in energy planning provided the main motivation for the use of MOO and MCA models and methods with a special evidence in scientific literature since the 1980s.
The increasing need to account for sustainability issues, which is inherently a multi-criteria concept, in planning and operational decisions, the changes in the organization of energy markets, the conflicting views of several stakeholders, the prevalent uncertainty associated with energy models, have made MOO and MCA approaches indispensable to deal with complex and challenging problems in the energy sector.

## Slide 4: The Energy sector and OR
MOO and MCA approaches are essential for a thorough analysis of energy problems at different decision levels, from strategic to operational, and with different timeframes.
Planning | Typical timeframe | Examples of decisions to be made
Long-term/Strategic | Several years-decades | Generation expansion planning Transmission facility expansion Siting of new power plants Energy-environment-economy models for policy design Market design
Operational | Months-years | Generation scheduling Transmission scheduling Reactive power planning
Short-term | Hours-days-weeks | Unit commitment Power flow Demand-side management
Categories of planning problems in power systems according to the
organizational level and time frame

## Slide 5: Energy-Environment-Economy models
The study of the interactions between the economy (at national or regional levels), the energy sector and the corresponding impacts on the environment inherently involves multiple axes of evaluation of distinct policies.
In general, MOO models for this purpose are developed based on input-output (IO) analysis or general equilibrium models (GEM).
The analytical framework of IO enables to model the interactions between the whole economy and the energy sector, thus identifying the energy required for the provision of goods and services in an economy and also quantifying the corresponding pollutant emissions.
GEM include interrelated markets and represent the (sub-)systems (energy, environment, economy) and the dynamic mechanisms of agent’s behavior to compute the competitive market equilibrium and determine the optimal balance for energy demand/supply and emissions/abatement.

## Slide 6: IO MOLP models (why?)
There has been a growing interest in scientific literature on the study of the causal relationship between energy consumption and economic growth and the corresponding environmental impacts.
This research avenue was triggered by the oil crisis in the 1970s, caused by the peaking of oil demand in major industrial nations
and embargoes from producer countries.
Although the nexus between energy consumption and economic growth has yielded mixed and inconsistent results in terms of their causal relationships, its appraisal is fundamental for the economic and energy decision-making process.

## Slide 7: IO MOLP models (Why?)
Many countries do not possess indigenous energy resources and generally depend on primary energy imports such as crude oil, natural gas and coal. In such situations a positive relationship between energy consumption and economic growth might be expected.
As a result, economic growth is usually responsible for an increase of energy consumption which heavily relies on fossil fuels, being both responsible for the depletion of finite resources and for the emission of Greenhouse Gases (GHG). Finally, energy and environmental policies may induce negative effects on economic growth and social welfare.
Therefore, the merits of energy plans and policies cannot be judged by considering just economic concerns, but other evaluation aspects such as environmental and social welfare impacts, should be explicitly taken into account to address energy problems in a societal perspective (Antunes and Oliveira, 2014).

## Slide 8: IO MOLP models (Why?)
Thus, it is particularly relevant for planners and decision-makers (DM) to assess the trade-offs between economic growth, energy demand/supply, as well as their corresponding environmental and social effects through the use of consistent tools for supporting the process of policy decision-making.
In this context, the use of multiobjective programming models and methods coupled with IO analysis seem particularly suited for helping in the process of (Energy-Environment-Economy-Social) E3S policy design.

## Slide 9: IO MOLP models (Why?)
Several countries compile IO tables for their economies at regular time intervals as a national statistical requirement providing an overarching framework that describes a coherent, consistent and integrated set of macroeconomic accounts forming a basis for economic analysis and policy formulation.
In this context, IO analysis is an analytical tool adequate for the evaluation of the inter-relations between different economic activities having evolved and being often applied to assess E3 interactions.

## Slide 10: IO MOLP models (Why?)
Less known, but also acknowledged is the fact that IO has influenced linear programming (LP) in its early development.
In fact, IO analysis may be regarded as a simple particular case of LP.
Inter/intra-sector relations embedded in IO analysis allow designing the production possibility frontier. LP models enable choosing the optimum level of activities to optimize a given objective function, satisfying the production sector relations imposed by IO analysis.
Finally, IO multiobjective linear programming (MOLP) models allow studying different efficient possibilities of production (i.e. output levels for each activity sector for which no other feasible solution exists that allows improving the value of a given objective function without worsening the value of, at least, other objective function) consistent with the conflicting and incommensurable axes of evaluation inherently at stake.

## Slide 11: Some basic features on IO
IO Analysis has been traditionally used to study the inter/intra-linkages between the different sectors in an economic system.
In its most basic form, an IO model consists of a system of linear equations, each one of which describing the distribution of an industry’s output throughout the economy.

## Slide 12: Some basic features on IO
The total output of an activity sector i (xi) is delivered for intermediate consumption and/or final demand. Equation (1) gives the distribution of the total output of each sector:
xi = (1)
where xi is the output of sector i, xij is the input from sector i to sector j, and yij is the input of sector i to final demand sector j.

## Slide 13: Some basic features on IO
Considering the hypothesis of constant returns to scale, Equation (1) becomes:
xi = (2)
in which the coefficients aij are the amount of input delivered by sector i to sector j per unit of sector's j output, also known as technological coefficients (or direct coefficients).

## Slide 14: Some basic features on IO
Analogously, equation (3) gives the total primary inputs of each sector:
xj = (3)
where zij is the primary input from sector i to sector j.
Then, similarly to (2) and considering (3), equation (4) is obtained:
xj = (4)
where the coefficients wij are the amount of primary input delivered by sector i to sector j per unit of sector’s j output.

## Slide 15: Some basic features on IO
The values of the transaction IO matrix may be then distributed by considering n activity sectors, m final demand sectors and p primary inputs .
Possible schematic representation of a classical IO transaction table

## Slide 16: Some basic features on IO
From (2), and considering final demand aggregated into a single vector, the productive system at a national level can then be represented in its matrix form following the basic IO system of equations (5):
x = Ax + y, (5)
where A is a matrix of technological coefficients, y is a vector of final demand, and x is a vector of the corresponding outputs.
In order to finally obtain the output multipliers, the Leontief inverse matrix needs to be derived. Equation (5) can then be rearranged to:
Ax + y = Ix  Ix – Ax = y  (I – A)x = y  x = (I – A)-1y, (6)
where I is the identity matrix with convenient dimensions and (I – A)-1 is also known as the Leontief inverse.
Each generic element of (I – A)-1 represents the total amount of good or service i directly and indirectly needed to deliver a unit of final demand of good or service j. In fact, the Leontief inverse indicates the direct and indirect requirements of production that are needed to satisfy a particular final demand vector.

## Slide 17: Some basic features on IO
Since the late 1960s the IO framework has been extended to account for environmental pollution generation and abatement associated with inter-industry activity .
Miller and Blair (2009) have considered three basic categories of environmental IO models:
  generalized IO models including additional rows and columns within the IO system to incorporate the pollution generation and abatement activities;
  economic ecological models utilizing intra/inter-sector sub-matrices linking the economic and ecosystems sectors;
  commodity by industry models expressing environmental factors as “commodities” in a commodity-by-industry IO table.
An external expansion of the IO framework can also be considered to incorporate the environmental impacts, assuming a proportional relation between the output of the sectors and the corresponding impact levels.

## Slide 18: Some basic features on IO
A very simple approach to accounting for pollution generation associated with inter-industry activity is to first assume a matrix of pollution output or direct impact coefficients, R, where each generic element, rkj, is the amount of pollutant type k, generated per monetary unit of industry j’s output. Therefore, the level of pollution associated with a given vector of total outputs can be expressed as:
r = Rx (7)
where r is the vector of pollution levels.
Thus, by considering (6) and (7) we can compute vector r as a function of final demand, that is, the total pollution of each type generated by the economy directly and indirectly in supporting that final demand:
r = R (I – A)-1y, (8)
Finally, from (8) we can interpret R (I – A)-1 as a matrix of total environmental impact coefficients; that is, an element of this matrix is the total pollution impact generated per monetary unit of final demand presented to the economy.

## Slide 19: Theoretical underpinning of IO MOLP models
Until now we developed the basic IO framework as the solution of a system of n linear equations with n unknowns leading to a unique solution.
The advantage of the IO approach lies in its mathematical simplicity, making its use practical for planning purposes.
In general, when using IO analysis for planning applications, the optimization (maximization or minimization) of some objective function related to inter-industry activity is usually considered.

## Slide 20: Theoretical underpinning of IO MOLP models
According to the IO model addressed previously, the left hand side of equation (6), states that net production of goods and services in an economy should equal final demand. However, this assumption may be relaxed to state that net production of goods and services should be greater or equal than final demand:
(I – A)x  y. (9)
When competing imports (of close substitutes of domestic goods or services) are explicitly considered the intersectoral flows contain both imported or domestically produced goods and services. Therefore, it is necessary to make adjustments to determine the correct domestic output, by treating competing imports as negative exports (Leontief 1985). Therefore (6) might be replaced by:
x = Ax + y –mc  x = (I – A)-1 (y – mc), (10)
where mc is the column vector of competing imports.

## Slide 21: Theoretical underpinning of IO MOLP models
Then, by relaxing (10), (9) is replaced by:
(I – A)x+ mc  y. (11)
Thus, from (11) it is possible to state that final demand of a good or service should never exceed the amount available both from net production and imports.
These are also known as the coherence constraints of the IO LP model.

## Slide 22: Theoretical underpinning of IO MOLP models
If the aim of the DM is to know what is the minimum value added (or the primary inputs - see (4)), z, that satisfies deliveries to final demand , the following notation is often used in specifying an LP problem:
min z = wTx,
s.t. (I – A)x  y,
x  0, (12)
where wT is a row 1x n vector of aggregated primary inputs.
The optimal solution to this problem satisfies the structural conditions of the IO model and it turns out that minimizing total value added as the objective subject to these conditions is equivalent to the original IO problem.

## Slide 23: Theoretical underpinning of IO MOLP models
However, the DM may be interested in finding combinations of x that satisfy these structural conditions but minimize pollution emissions or energy consumption or perhaps any other factor that is assumed to vary with industry output.
An important advantage of the IO LP framework is that alternative objective functions and/or additional constraints can be considered as part of the planning problem.
The LP formulation to the generalized IO planning problem provides enough flexibility to include alternative or even multiple objective functions in approaching planning problems.

## Slide 24: IO hybrid approaches
Some studies also apply IO models using hybrid frameworks considering energy flows in physical quantities of energy (eg. tons of oil equivalent – toe) and all non-energy sector flows in monetary units.
Since in general the energy sectors produce more than one energy product, the problem of how much environmental burden should be attributed to each energy product arises.
In this case artificial sectors may be considered to make the distribution of the outputs of the energy producing sectors, thus enabling to individualize the consumption of each form of energy. This is required, for instance, to compute the corresponding pollutant emissions.

## Slide 25: IO hybrid approaches
A possible schematic representation of the constraints based on the IO framework of such models is provided in the next Figure.
 | Energy and Non-Energy branches | Final demand | Competitive imports | National output | Constraints
Energy and Non-Energy Branches | a) Ax | b) Dy | mc | x | Ax + y ≤ mc + x
Energy Branches | a) AEx | b) DEy | mEc | xE | AEx + yE ≤ mc + xE
Primary inputs | Intermediate consumption | Final demand |  |  | 
Non-energy imports | c) Am x | e) Dm y |  |  | Am x + Dm y
Energy imports | d) Amnc x | f) Dmnc y |  |  | Amnc x + Dmnc y
Net taxes (ts) | g) Ats x | h) Dts y |  |  | ts = Ats x + Dts y
Gross value added (gva) | i) wages (awT x) |  |  |  | gva = awT x + + atT x - asT x + + aosT x
 | other net taxes i) (atT x - asT x) |  |  |  | 
 | i) gross operating surplus and gross mixed incomes (aosT x) |  |  |  | 
Employment (emp) | j) lT x |  |  |  | emp = lT x

## Slide 26: IO hybrid approaches
Technical coefficients (product-by-product/sector-by-sector) matrix (composed of sub-matrices A and AE). Each element is the amount of good or service i needed to produce a unit of good or service j. This matrix is given in hybrid units.
Diagonal matrices (DE and D) whose main diagonals correspond to the coefficients of consumption of energy and/or non-energy commodities by the final demand sectors (households and non-profit institutions serving households - NPISH, public consumption investment, GFCF - gross fixed capital formation, ALDV - acquisitions less disposals of valuables and stock changes and exports).
Matrix of non-competitive import coefficients of non-energetic goods or services (Am).
Matrix of non-competitive import coefficients of energy (Amnc).
Diagonal matrix (Dm) whose main diagonal is the vector with the weights of non-competitive imports of non-energetic goods or services aimed at household/ NPISH/ public consumption/ GFCF/ changes in inventories/ ALDV on the total household/ NPISH/ public consumption GFCF/ changes in inventories/ ALDV, respectively.
Diagonal matrix (Dmnc) whose main diagonal is the vector with the weights of non-competitive imports of energetic goods aimed at household/ NPISH/ public consumption/ GFCF/ changes in inventories/ ALDV/ exports on the total household/ NPISH/ public consumption GFCF/ changes in inventories/ ALDV/ exports, respectively.
Matrix with the weights of net taxes on goods and services on the total output of each branch (Ats).
Diagonal matrix whose main diagonal is the vector with the weights of net taxes on goods and services aimed at household/ NPISH/ public consumption/ GFCF/ changes in inventories/ ALDV/ exports on the total household/ NPISH/ public consumption GFCF/ changes in inventories/ ALDV/ exports, respectively.
aw, at, as, aos are the vectors with the weights of wages/ taxes/ subsidies/ gross operating surplus and gross mixed incomes on the total output of each branch.
The employment level is obtained by using labour gross productivity coefficients (lT) for each branch.

## Slide 27: IO hybrid approaches
Energy branches
Possible schematic representation of the energy system.
23 | Oil refining sector
40.1 | Electricity distribution
A17 | Co-generation
A18 | Eolic and others
A19 | Geothermal
A20 | Hydroelectricity
A21 | Thermoelectricity
40.2 | Distribution of gas by pipeline
A22 | Distribution of natural gas
A23 | Distribution of city gas
40.3 | Distribution of hot water and steam
M1 | Coal (includes anthracite) and lignite
M2 | Crude oil
M3 | Oil wastes and intermediate products
M4 | Natural Gas
M5 | Petroleum coke
 |  | Energy branches |  |  |  | Electricity products |  |  |  |  | Refinery products | Gas products | Non-energy branches
 |  | 23 | 40.1 | 40.2 | 40.3 | A17 | A18 | A19 | A20 | A21 | A1 to A16 | A22, A23 | 
Energy | 23 |  |  |  |  |  |  |  |  |  | x |  | 
 | 40.1 | x | xa) | x | x |  |  |  |  |  |  |  | x
 | 40.2 |  |  |  |  |  |  |  |  |  |  | x | 
 | 40.3 | x |  | x |  |  |  |  |  |  |  |  | x
Electricitity | A17 |  | x |  | x |  |  |  |  |  |  |  | 
 | A18 |  | x |  |  |  |  |  |  |  |  |  | 
 | A19 |  | x |  |  |  |  |  |  |  |  |  | 
 | A20 |  | x |  |  |  |  |  |  |  |  |  | 
 | A21 |  | x |  |  |  |  |  |  |  |  |  | 
Refinery products | A1 to A16 | xa) | xb) | x |  | x |  |  |  | x |  |  | x
Gas | A22, A23 | x | x | xa) |  | x |  |  |  | x |  |  | x
Non-energy branches |  | x | x | x | x |  |  |  |  |  |  |  | x
Non-competitive energy imports | M1 to M5 | x | x | x |  | x |  |  |  | x |  |  | x
x – Square with significant value.
a) Losses regarding transport and distribution.
b) Consumptions regarding transport means.

## Slide 28: IO hybrid approaches
Suppose that we expand our IO LP model to include several alternative technologies for non-energy sectors.
If we want to account for systems with multiple products, they generate matrices with more rows than columns.
In this context, the LP formulation is able to tackle the representation of alternative technologies. Therefore, detailed models of important industry sectors are often used for decision support.
This hybrid approach of linking detailed models with aggregated, economy-wide models is the current focus of research in Life Cycle Assessment (LCA). In particular IO LCA and process LCA can be linked to combine their strengths.

## Slide 29: IO hybrid approaches
 | Other Activity sectors j | Activity sector with technologies T | Final demand | Total Output | Constraints
Products of activity sector i |  |  | yi | xi | + + yi ≤ xi
Products (p) of activity sector j with T technologies |  |  | yp | xp | + + yp ≤ xp
The total output xi of goods and services i must be greater or equal than the intermediate demand from sectors j, from the technologies T and final demand yi.
Similarly, the total output xp of products p must be greater or equal than intermediate demand from sectors j, from the technologies T, and final demand yp.

## Slide 30: IO in the framework of MOLP models
Until now we have considered problems with a single objective; however, strategic decisions are made in an increasingly complex and changing environment.
In addition, reality is inherently characterized by multiple, conflicting and incommensurable axes of evaluation. For this reason, mathematical models for decision-making in planning problems become more representative of reality if the multiple aspects of evaluation of the merits of distinct potential policies (solutions) are explicitly considered. Thus, environmental, economic and social concerns, for example, should be explicitly considered and not combined into a single economic indicator.
Multiobjective models allow capturing the diverse nature of the aspects of evaluation, often conflicting and non-commensurate, where the DM is faced with the need to seek compromises between objectives, since, in general, there is no feasible solution which simultaneously optimizes all objective functions.
In a multiobjective context, the concept of optimal solution, considered in models with a single objective, gives rise to the concept of efficient or non-dominated solutions (feasible solutions that cannot improve an objective function without sacrificing at least one of the other objective functions).

## Slide 31: IO in the framework of MOLP models
In a general, a MOLP problem is formulated in the following way:
Min (or z1 = )
....
min (or zp = )
s.t. , i=1,...,m ( or )
, j=1,...,n (13)
where are row 1n vectors, each one corresponding to an objective function.

## Slide 32: IO in the framework of MOLP models
For example, if a DM is interested in minimizing the value added cost to meeting a target final demand, minimizing pollution emissions and energy conservation all as objectives, problem (12) becomes:
min z1 = wTx,
min z2 = rT1 x,
min z3 = rT2x,
s.t. (I – A)x  y,
Rx  r,
x  0. (14)
where rT1 and rT2 are row 1n vectors of the impact matrix R (see (5)), each one corresponding to pollution emissions and energy conservation objective functions.

## Slide 33: IO in the framework of MOLP models
There are several methods available in the scientific literature to find an efficient solution to problems (13) and (14). Methods for solving MOLP problems may be classified according to the intervention degree of the DM:
a) A priori articulation of the DM’s preferences – once the method is chosen (and, possibly, some parameters fixed), the preference aggregation is settled.
The most commonly used are:
i) the method of the minimum distance to the ideal solution according to a certain metric;
ii) methods where an utility function is used, built from the objective functions of the original problem;
iii) the lexicographic method where the objectives are sequentially optimized and equality constraints based on the objective function values may also be sequentially added to the next optimization problems;
iv) and goal programming.

## Slide 34: IO in the framework of MOLP models
b) Progressive articulation of the DM’s preferences - the interactive methods have a succession of computation and dialogue phases. After each computation phase an efficient solution (or several) is (are) proposed to the DM that reacts by providing the necessary information to operate a new computation phase, or by stopping the procedure. The characteristics of the dialogue and computation phases, as well as the stopping conditions of the interactive algorithm depend on the method.
The most commonly reported in scientific literature for solving IO MOLP models are:
i) The Step Method (STEM) developed by Benayoun et al. (1971) is an interactive method that progressively reduces the feasible region. In each interaction, the DM is asked to specify the amount that he/she is willing to sacrifice in the objective function whose value he/she considers more satisfactory, in order to improve those whose values do not satisfy him/her. In each computation phase a weighted Tchebycheff distance to the ideal solution is minimized.
ii) The TRIMAP method, developed by Clímaco and Antunes (1987, 1989), combines a set of procedures, which allow a free search based on the progressive and selective learning of the set of efficient solutions. It combines the reduction of the feasible region with the reduction of the parametric weight space. The DM is able to specify the lower bounds for the objective functions and/or impose constraints on the parametric weight space. In each computation phase a weighted sum of the objective functions is optimized.

## Slide 35: IO in the framework of MOLP models
iv) The Zionts and Wallenius (1976, 1983) method reduces progressively the weight space, according to the DM’s preferences. In each computation phase a weighted sum of the objective functions is optimized. The procedure stops when the weight space is reduced to a sufficiently small region, in a way that it is possible to identify a final solution, or when the information of preferences expressed by the DM indicates that the current solution is the most interesting one.
iv) The SOMMIX interactive environment is based on a control panel (embodying search strategies, techniques to compute new efficient solutions, ways to express the DM’s preferences, means of interaction and information presentation) to assist the user by facilitating and motivating the successive actions throughout the interactive solution search process (Clímaco et al., 1997).

## Slide 36: IO in the framework of MOLP models
c) A posteriori articulation of preferences - methods for generating the entire set of efficient solutions where the aggregation of the DM’s preferences is made after the set of efficient solutions is generated. The methods for generating the set of efficient solutions may be split into two fundamental categories:
  i) Approximation methods - the most representative are: the weighting method; the e-constraint method; and the method for estimating the set of non-inferior solutions (NISE).
  ii) Exact methods - the most significant is the multiobjective simplex method (having several versions).

## Slide 37: IO in the framework of MOLP models
An also commonly applied extension to LP to accommodate multiple objectives is known as multiple goal programming (GP). In its most general form the multiple GP problem (tries to minimize the deviation regarding the targets established by the DM) can be formulated as :
However, the targets established by the DM may lead to a feasible solution that does not belong to the set of efficient solutions. In this context, this means that the DM has little ambition when defining the targets that he/she wants to achieve. In order to prevent this from happening, the analyst should advise the DM to formulate targets ambitious enough.

## Slide 38: IO in the framework of MOLP models

## Slide 39: Uncertainty handling of IO MOLP models
In general, the technical coefficients of the IO matrix are not exactly known and are subject to a considerable level of uncertainty .
The uncertainty sources of IO models may be the result of the incoherence of data from several sources or even from the assumptions inherent to IO analysis (linearity and proportionality, for example) or from the aggregation level of the sectors considered.
The uncertainty handling in the framework of IO analysis may be fundamentally based on three different approaches:
  the probabilistic approach where the probabilistic distribution functions associated with all the coefficients are presumably well known (e.g. West, 1986; ten Raa and Steel, 1994);
  the interval approach (unknown but bounded coefficients), where the upper and lower bounds of the coefficients are considered without being associated with a structure of possibilities or probabilities (e.g. Jerrel, 1996; Jerrel ,1997);
  and the fuzzy (or possibilistic) approach, where the membership functions are assigned to all uncertain coefficients (e.g. Buckley, 1989).
From the approaches herein mentioned interval programming possesses some interesting characteristics, since it just assumes that information about the range of variation of some (or all) coefficients is available.

## Slide 40: Uncertainty handling of IO MOLP models
Interval Programming has been used to tackle specific issues in MOLP.
In this sense, some algorithms only deal with uncertainty in the objective functions, others handle uncertainty both in the objective functions and in the right hand side (RHS) of the constraints, and others deal with uncertainty in all the coefficients of the model (Oliveira and Antunes, 2007).
Two different approaches to deal with an interval objective function are commonly considered: the satisficing approach and the optimizing approach.
In the satisficing approach each interval objective function is transformed into one or several objective functions (the lower bound, the upper bound and the central value of the intervals are usually used) in order to obtain a compromise solution.
Although the compromise solution obtained in this way is efficient, it might not be the most suited one to the interval MOLP problem. In fact, if the gradients of the chosen objective functions are highly correlated, the scope of the search might be reduced and ultimately the gradient cone of each objective function becomes a ray.
On the other hand, the optimizing approach extends the concept of efficiency used in traditional MOLP to the interval objective function case.

## Slide 41: Uncertainty handling of IO MOLP models
The problem regarding the application of these approaches in the framework of IO MOLP models refers to the fact of not considering the uncertainty handling of the IO technical coefficient matrix, only allowing for the incorporation of uncertainty in the objective functions.
The interactive approaches developed by Urli and Nadeau (1992) and Oliveira and Antunes (2009) are particularly adequate for tackling the uncertainty handling of IO MOLP models, since they may be applied to MOLP models with interval coefficients in the whole model.

## Slide 42: Methodologies for tackling the uncertainty
Interval Programming
are closed intervals
where
s.t.

## Slide 43: An interval model for E3 planning
Objective functions
Axes of evaluation
Economy
Max (GDP)
Environment
Min (GHG)
Energy
Min (Energy imports)
Social
Max (Employment)
Interval
Interval

## Slide 44: An interval model for E3 planning
Constraints
  Coherence constraints
  Defining constraints – Upper/Lower bounded
  Constant prices
    Private consumption
    Exports CIF/FOB, Imports CIF/FOB, Available income
    net taxes on goods and services
    GDP
    Public consumption, GPFCF, Stock changes, ACOV
    gva = awagT x + aotT x – aosT x + aOpSurplusT x
Interval
Interval
Ax + cptf + csf + g + fbcf + acov + (sc+ – sc-) + expb  x + impc
= 0 + 1 (yd )
prc + g + gfcf + sc + acov + expfob – mfob
gdpprod = gav + ts

## Slide 45: An interval model for E3 planning
Constraints
  Defining constraints – Upper/Lower bounded
  Current prices
    GDP = (prc) (prcp) + gcurr + gfcfcurr + (sc) (scp) + (acov) (acovp) + + (expfob) (expfobp) – (mfob) (mfobp)
    Available income = corrgdp (1 – pspibcorr) + (pr+ – pr- + tisub – tisubg) + + tre – td – tdsc – css – tisub – (repg+ – repg-) + trig
    Public debt = div-1 – (sgg+ – sgg-) + dat
    PAS Global Balance = td + tdsc + css + tisubg + repg+ – repg- – gcorr – trig + + treg – jurg + tk + trkg – gfcfg
Interval

## Slide 46: An interval model for E3 planning
Constraints
  Defining constraints – Upper bounded
  Environmental indicators
    GHG = etco2 + (310) (etn2o) + (21) (etch4)
    Acidifying emissions = (21.74) etnox + (31.25) etso2 + (58.82) etnh3
    Ozone precursors emissions= (1.22) (etnox) + etcovnm + (0.11)(etco) + (0.014) (etch4)
Interval

## Slide 47: Uncertainty handling of IO MOLP models
Finally, when multiobjective stochastic linear programming can be used as a modelling approach, Urli and Nadeau (2004) developed a scenario approach, called PROMISE/scenarios, where the probabilities of scenarios are only incompletely specified according to a ranking. However, this method is either suited for models with small dimensions or for big dimensional models but with few scenarios.

## Slide 48: A review on IO MOLP models
Main scopes and applications of IO LP models.
In general, traditional studies using IO analysis under the framework of LP consider a given regional economy and can be used for economic purposes or even for energy/environmental planning and waste/wastewater management.

## Slide 49
Main scope | Application | Country | Reference | Citations (google scholar)
Economic planning | Choose gross output to minimize labour costs of a specified bill of final goods | USA | Dorfman et al. (1958) | 2124
Economic planning | Explain how do changes in the structure of inputs influence the output level of particular activity sectors | Poland | Lipinski (1985) | n.a.
Economic planning | Determine comparative advantages in international trade | Canada | ten Raa and Mohnen (1994) | 21
E3 planning | Determine the optimal extent of economic activities within the restrains set to environmental pollution and optimal allocation of scarce oil products | Netherlands | Muller (1979) | 43
Energy planning | Evaluate the impacts of energy shortages | Hawaii | Leung and Hsu (1984) | 11
Economic planning | Obtain a balanced level of production of sectors producing capital goods with the amounts of financial resources available for these sectors | USSR | Kazantzev (1985) | n.a.
Regional energy planning | Help the Advisory Board on Energy of the government of India to envisage regional energy planning, capturing regional specificities in the energy demand-supply structure | India | Moulik et al. (1992) | 6
Waste management | Establish how sustainable consumption should be | Japan | Kondo and Takase (2003) | 1
Waste management | Obtain an optimal waste management and recycling strategy among a given set of alternative feasible strategies | Japan | Kondo and Nakamura (2005) | 35
Wastewater management | Obtain the optimal wastewater treatment options under alternative scenarios | Japan | Lin (2011) | 6
E3 planning | Reallocate production in Greece, on a sector-by-sector basis, in order to meet overall demand constraints and GHG Kyoto emission targets | Greece | Hristu-Varsakelis et al. (2010) | 7
E3 planning | Quantify the magnitude of economic sacrifices required to achieve environmental goals, in a series of policy scenarios of practical importance | Greece | Hristu-Varsakelis et al. (2012) | n.a.

## Slide 50: A review on IO MOLP models
Main scopes and applications of IO MOLP models.
IO MOLP models can provide a more complete assessment of different axes of evaluation of potential policies, enabling to exploit the trade-offs between competing objectives.
These IO MOLP models have been applied to provide support on economic/energy/environmental planning, wastewater management, operations planning, supply chains management and crises management (e.g. nuclear power plant accidents, trade embargoes and international conflicts).

## Slide 51
Main scope | Application | Country | Reference | Citations (google scholar)
Macroeconomic planning | Assess trade-offs between Gross National Product (GNP), the trade deficit and the employment | Bangladesh | Quaddus et al. (1985) | 2
E3 planning | Assess trade-offs between GDP and energy use | Taiwan | Hsu et al. (1987) | 12
Crises management (nuclear power plant accidents, trade embargoes, and international conflicts) | Study the quantitative effects of economic or political crises to the economy. | Finland | Kananen et al. (1990) | 28
Regional economic/energy planning | Present some computational experiments using a regional planning model | Portugal | Alves et al. (1997) | 1
Energy planning | Examine the trade-offs between economic and environmental objectives in the power sector | Japan | Amagai and Leung (1991) | 13
Environmental planning | Focused on model formulation | n.a. | Luptáčik and Böhm (1994) | 12
E3 planning | Obtain a balanced policy configuration | South Korea | Cho (1999) | 25
E3 planning | Evaluate the impact of energy conservation policies | Taiwan | Hsu and Chou (2000) | 36
Wastewater management | Reveal the dynamic relationships between the rapid economic development, water pollution and the waste-load allocation in different economic sectors | China | Ni et al. (2001) | 16
E3 planning | Assess the interactions of the energy system and the economy by means of a graphical tool | Portugal | Antunes et al. (2002) | 8
E3 planning | Provide decision support to planners and decision makers by means of an interactive method | Portugal | Oliveira and Antunes (2002) | 9
E3S planning | Provide decision-makers with a comprehensive model which allows to assess environmental burdens | Portugal | Oliveira and Antunes (2004) | 62
Economy-energy planning | Analyse and choose alternative versions of the development of the real sector of the national economy | Belarus | Kravtsov and Pashkevich (2004) | 5
Operations planning | Evaluate the operation of a Combined Heat and Power(CHP) eco-industrial park | China | Jing and Chun-you (2007) | n.a.
Environmental-Economy planning | Estimate the macroeconomic costs of CO2 emission reduction in China | China | Fan et al. (2010) | 2
Supply chains management | Obtain the optimal design and planning of cellulosic ethanol supply chains | USA | You et al. (2012) | 117
E3 planning | Assess the effects of a reduction in greenhouse gasses emission and energy requirements | Spain | Cristóbal (2012) | 4
E3 planning | Identify trade-offs between GDP, employment level, energy consumption and GHG emissions | Brazil | Carvalho et al. (2013) | n.a.

## Slide 52: A review on IO MOLP models
Main scopes and applications of IO LP/MOLP models with uncertainty handling techniques.
In most real world problems there is not enough information to allow for the accurate specification of the coefficients of the objective functions and the constraints of optimization models. Thus, it is convenient to consider the extension of mathematical models for decision support environments where uncertainty exists, without taking for certain the crisp nature of the model coefficients.
Therefore, both IO LP and IO MOLP models, which explicitly incorporate the uncertainty handling of the model coefficients have also emerged in scientific literature.

## Slide 53
Main scope | Application | Uncertainty handling Tool | Country | Reference | Citations (google scholar)
E3 planning | Examine approaches to achieve the integration of environmental concerns in power sector and evaluate impacts on economic and energy sector for each of these strategies | Fuzzy programming | Taiwan | Chang and Juang (1998) | n. a.
Economy-energy planning | Provide decision support to DM in the study of interactions between the energy system and the economy on a national level | Fuzzy programming | Portugal | Borges and Antunes (2003) | 63
Supply chain management | Assess the ecological footprint of activities associated to an enterprise or region in the consumer or producer’s perspective | Fuzzy programming with multiple DM | Republic of the Philippines | Aviso et al. (2011) | 24
Biomass production planning | Optimize biomass production and trade | Fuzzy programming | Republic of the Philippines | Tan et al. (2012) | 22
E3 planning | Explore the effects of distinct policies on the total system costs, the fuel and technology mix, and the levels of greenhouse gases and other emissions. | Interval programming | Portugal | Oliveira and Antunes (2011) | 22
E3 planning | Discuss the influence of austerity measures on economic growth, social well-being, energy consumption as well as its impacts on the environment | Interval programming | Portugal | Oliveira and Antunes (2012) | 6
RES-E jobs generation | Discuss the various factors that influence the appraisal of sustainable systems integrating environmental, social and economic dimensions, mainly focusing on RES-E jobs generation | Interval programming | Portugal | Oliveira et al. (2013) | 1
Energy Efficiency investment planning in the building sector | Assess the trade-offs between the overall employment, GDP and energy savings associated with the building sector | Interval programming | Portugal | Oliveira et al. (2014a) | n.a.
Uncertainty handling | Overcome the inexactness and limitations regarding the entries of the IO coefficients’ matrix | Robust optimization | China | Wen et al. (2014) | n.a.

## Slide 54: A review on IO MOLP models
Main scopes and applications of LP/MOLP dynamic IO models.
In order to account for the growth potential of an economy, Leontief developed the dynamic IO model, where a new matrix describing the capital resources is considered, aimed at distinguishing different technological structures in different time frames.
With this formulation, the final demand vector of the static IO model is replaced by a stock coefficient’s matrix that is then multiplied by the anticipated increase of the output level between the present year and the subsequent year.
This new set of differential equations represents the dynamic relations of the IO model, allowing for the description and analysis of the economic growth process. Therefore, the applicability of dynamic IO analysis based on both LP and MOLP frameworks was also studied in recent years.

## Slide 55
Main scope | Application | Country | Reference | Citations (google scholar)
Inventory management | Examine the impact of optimal use of imported inventories for public enterprises, public limited companies and private limited companies | India | Prasad et al. (1996) | 1
Regional Economic planning | Regional and macroeconomic forecast | China | Zhang et al. (2001) | 2
Regional Economic planning | Regional and macroeconomic forecast | China | Zhou et al. (2004) | 2
Regional Economic planning | Investigate the mechanism of the instability of the original MODIO models theoretically and development of a modified MODIO model. | China | Zhou et al. (2006) | 2
Renewable industries and environmental policy planning (emission tax) | Explore the relationships among renewable energy, economy and environment and analyse the future trends of the economy and GHG intensity. | China | Zou et al. (2014a) | n.a.
Economy and environmental policy planning (emission tax) | Explore the relationships between the economy environment and analyse the future trends of the economy and GHG intensity. | China | Zou et al. (2014b) | n.a.

## Slide 56: A review on IO MOLP models
Main scopes and applications o IO f LP/MOLP models with DEA.
The eco-efﬁciency of the economy can be obtained as a solution of a Data Envelopment Analysis (DEA) model with the virtual decision-making units (DMUs) deﬁning the potential and a DMU describing the actual performance of the economy.
This model combined with IO analysis allows taking into account the interdependences of the sectors in an economy in eco-efﬁciency analyses.
Through the use of MOO models an eco-efﬁciency frontier of the economy can be generated. The solutions of the multiobjective optimisation problems deﬁne eco-efﬁcient virtual DMUs. Furthermore, it permits estimating eco-efﬁciency of an economy with respect to its own potential and without the need to compare it with other economies – economies that may possess different technologies and varying mutual interdependencies due to international trade (Mahlberg and Luptacik, 2014).

## Slide 57: A review on IO MOLP models
Main scopes and applications o IO f LP/MOLP models with DEA.
Main scope | Application | Country | Reference | Citations (google scholar)
Efficiency analysis | Analyse the eco-efﬁciency of an economy | Austria | Luptacik and Böhm (2010) | 8
Efficiency analysis | Analyse the eco-efﬁciency of an economy, considering the eco-efficiency change | Austria | Mahlberg and Luptacik (2014) | 2

## Slide 58: A review on IO MOLP models
MOLP techniques for updating the IO matrix
Multiobjective optimization techniques can also be used as an adjustment/updating procedure of the IO matrix.
Peñate and Peñate (2003) suggested the use of this kind of tools to update the IO matrix included in the social accounting matrix (SAM) concentrating in the vertical/column/technical coefficients.
The method proposed can be also applied to situations where the adjustment criteria are not the same for different parts of the SAM. Using the benchmark SAM as the basis, and incorporating the new information available, a biobjective problem is used where both the vertical and horizontal adjustment are combined.

## Slide 59: Conclusions
IO analysis is a flexible and interesting tool for theoretical or empirical studies of a wide variety of problems ranging from microeconomics to macroeconomics, which can be used to modelling complex systems of economic and physical interrelations.
In fact, IO analysis provides an important tool to assess any type of environmental burdens caused by changes in the output of economic sectors once reliable economic data is used.
The application potential of this tool of analysis coupled with mathematical programming models as a planning and prospective analysis tool has led to the proposal of several IO MOLP models which allow obtaining a broad range of indicators (economic, social, energy and environment) according to coefficient scenarios and to the output level attained for the economic sectors (industries). For instance, the use of DEA in the framework of IO MOLP analysis allows taking into account the interdependences of the sectors in an economy in eco-efﬁciency analyses.
The IO MOLP framework has also been extended and adjusted to accommodate the uncertainty handling of the coefficients of this kind of models, overcoming a major drawback usually mentioned in scientific literature, which is related to the static nature of the IO traditional matrix.

## Slide 60: Conclusions
Future work on extending the IO MOLP model framework should consider the developing of a dynamic, multi-period variant. Such an extension can also integrate time-dependent technical parameters to account for technological learning curves and yield improvements, as well as incorporate game theoretic principles to accurately reflect the multi-agent nature of the problem.
Since usually these models only account for one DM (which most of the times is hypothetical and not real) another interesting line of research could be the development of tools for obtaining solutions, but considering the interaction with multiple real DMs with potentially conflicting views. The involvement of the interest groups may contribute in a positive way to the decision-making process at all its stages, from the method of defining the problems and objectives to the evaluation of possible solutions.
Also, the use of non-linear fuzzy membership functions can be explored in the future or even other uncertainty handling techniques such as the tolerance approach (eg. Ravi and Wendell, 1989) specifically developed for analysing the stability of solutions obtained regarding changes in the technical coefficients matrix. Significant non-convexities may result from such extensions. Therefore, it will also be necessary to develop solution algorithms to ensure that globally optimal, or near-optimal, solutions can be found.

## Slide 61
Drawbacks | Possible Solutions
Single outputs – The simplistic presumption that the transactions table within IO analysis assumes that commodities and sectors can be classified in the same way. Moreover, it suggests that sectors have multiple inputs, but only single outputs (ten Raa ,1994). | In order to accommodate this shortcoming, Stone (1966) has suggested accounting for inputs and outputs separately. Input flows may be framed in a use table, U, and output flows in a make table, V. The convention is that the dimensions of matrices U and V are commodities × sectors and sectors × commodities, respectively (ten Raa, 1994). The traditional transactions table may be recovered if V is diagonal. In this case, A=UV-1. However, in general V features non-zero off-diagonal elements, since sectors produce mixtures of outputs. In such cases, the problem of constructing an IO matrix, either X or A, is therefore non-trivial. Alternative methods to deal with this issue exist and are described by Viet (1994). Whatever model is employed, some matrix of technical coefficients, A, comes out of it and may be used in the equations of IO analysis.
Specialization - When an economic problem is formulated mathematically as an LP problem, typically, the number of active variables is no more than the number of constraints (ten Raa, 1994). Then when the value of the national product is maximized subject to the material balance constraints and the primary factor constraints, the former are binding and can be used to express national product components in sectoral activity levels. This elimination procedure leaves only the primary factor constraints to bind the sectoral activity levels and, therefore, the number of active sectors will match the number of primary factors. The extreme behaviour of IO models is believed to be caused by the assumption of non-substitutability of inputs of a technique. | Whenever the proportions of final demand of goods are fixed by consumption and trade coefficients, the fixed primary input proportions can be associated with components of the vector of final demand of goods and are weighted. In this case the national economy is implicitly modelled by a Leontief macroeconomic production function and specialization behaviour usually occurs in the form of some zero shadow prices of factor inputs. These observations pertain to standard IO LP models (e.g. Dorfman et al., 1958). The proportions of goods for final demand may vary freely and, therefore, the aggregate factor intensities also. Since the objective function is a linear valuation of net outputs, the latter are perfect substitutes and, since factor intensities vary across net outputs, there is some degree of substitution between factor inputs as well (ten Raa, 1994). So this extreme behaviour may be avoided.
Closing the model – The use of IO multipliers is particularly appropriate for evaluating the contribution of a particular industry to the economy and for performing the impact assessment of broad policy instruments. Therefore, there is a relevant potential to strengthen the relevance of LP and MOP IO, namely by closing the model (allowing for the calculation of induced impacts). | Usually this problem arises when hybrid IO unit’s matrices are used. In this situation it is enough to consider the equivalent monetary unit’s matrix (e.g Oliveira et al., 2013).

## Slide 62
Drawbacks | Possible Solutions
Specifying Objectives - It is important to note that IO MOLP and GP IO models provide considerable flexibility in handling multiple, even conflicting objectives. In LP it is only required to begin with a feasible region in order to find an optimal solution. In GP the feasible region is essentially unspecified since any point can be completely specified in terms of the deviational variables and it is the priority order of objectives that determines the solution, because by specifying a priority order a solution can be found even if the objectives are conflicting. This places much more of the planning burden on determining the priority order, which in a policy context is often quite complex, especially with sometimes competing policy objectives, such as economic growth and environmental quality. | Several methods can be used to establish priorities between objectives (Antunes and Henriques, 2014). The involvement of the interest groups at this stage is also important. The selection of the most efficient technique of involving public and the interest groups is a key to the success of the whole process. There is no “correct” technique suiting all situations. It is only rarely possible to stick to the “pure” models. Several available methodologies might be seen for example in Voinov and Bousquet (2010) and Manetti (2011).
Tightly Constrained Problems – Another commonly cited limitation of IO LP models and IO MOLP models is that the feasible region is very tight (eg. Antunes et al., 2002; Oliveira and Antunes, 2002; 2004; Carvalho et al., 2013; Miller and Blair, 2009) | For the GP IO case several solutions for this problem are indicated in Lane (1970). For the case of IO LP and IO MOLP problems, the concept of “elastic programming” introduced by Brown and Graves (1975) can be used to widen the feasible region. This method consists in the addition of extra variables (the “elastic variables”), which allow constraints to be relaxed thus enlarging the feasible region. A LP problem is then solved based on “the smallest variable cost model" (see Brown and Graves (1975), Chinneck and Dravnieks (1991) and Murty et al. (2000)). According to this model, the resistance to “stretch” implied by the term elastic is supplied by creating a new objective: minimize the sum of the total variable cost of all changes (that is, of the elastic variables). If this problem leads to a solution where the elastic variables are positive, then an optimal change of the RHS is obtained.
Single production processes - IO models include sectors rather than simple processes and sectors may be too heterogeneous to correctly reflect particular processes. | It is possible to expand IO LP model to include several alternative technologies. LP formulation is able to account for alternative technologies (Vogstad, 2009). There are hybrid approaches that allow linking detailed models with aggregated, economy-wide models. Vogstad (2009) shows how IO and a more detailed LP model of a sector can be integrated.

## Slide 63
Drawbacks | Possible Solutions
Static structure – The consideration of a similar technology without allowing the replacement of production factors may restrain IO analysis to short run economic analysis. | Two major issues are mixed up when this assumption is considered regarding short-run and long-run (Wilting et al., 2004). If a model is used for long-run studies it is desirable that the model incorporates technological changes. In general, the short-run technology options are limited since each industry has a certain type of technology installed, which does not allow for significant input replacement in the short-run. In the long-run one industry will have the opportunity of choosing several technologies with different input structures. There are basically two ways to incorporate technology changes in the framework of IO analysis: one is associated with trends and the other is based on experts opinions (e.g. Leontief e Duchin, 1986).
Use of monetary units when dealing with energy sectors – Several studies that account for technical coefficient of energy sectors in the IO table are based on the monetary units. This fact may change the results obtained when the wholesale price index or the exchange rate in an economy varies significantly. | The hybrid frameworks considering energy flows in physical quantities of energy (eg. tons of oil equivalent – toe) and all non-energy sector flows in monetary units is a possible solution (eg. Antunes et al., 2002; Oliveira and Antunes, 2002, 2004, 2011, 2012; Carvalho et al., 2013; Oliveira et al., 2013; Oliveira et al., 2014a; Borges and Antunes, 2003).